## Slide 1
Axial Flux Permanent Magnet Machine with
Novel Flat Winding
Made of Conductor Sheet
Gökhan Çakal
MSc Thesis Defense
September 2020
METU, Department of Electrical and Electronics Engineering Ankara, TURKEY
Notes: Dear professors and collagues

## Slide 2
Flat winding and implementation on AFPM
Analytical modeling
Experimental verification
1 MW wind turbine generator
Conclusions
Outline

## Slide 3
Existing Winding Topologies
Merits | Low eddy current loss | Fill factor Superior current | Easy to manufacture | Easy to manufacture
Challenges | Limited current density (5-6 A/mm2) Low current rating Manufacturing | Eddy current loss High cost Manufacturing | Eddy current loss High cost | High cost Low current ratings Low power
[1]
[2]
[3]
Conventional stranded round wires
Hairpin winding
Cast produced winding
PCB winding
Notes: Current density under air cooled 5-6 A/mm2
Manufacturing için winding machine gerekli
Parallel connections

## Slide 4
Proposed Solution: Flat Winding4
Take a thin conductor sheet
Cut pieces with
  Stamping press
  Laser cutter
  Water jet
Bend them
Place isolation papers between flat wires
Solder end windings
Mold with epoxy
Create terminals
[4] G. Cakal and O. Keysan, (2019). Elektrik Makinaları İçin Bir Sargı Yöntemi (Patent Pending). Türk Patent.
Notes: Patent pending
Gercek flat wire goster

## Slide 5
Merits
Ease of manufacturing
  Commonly used tools
High current density
  7 A/mm2 under natural cooling
Superior current ratings
  Eliminating parallel connection
Decreased end winding length
  Reduced end winding losses
Challenges
Merits and Challenges of Flat Winding
Flux passing direction
Laser cutting of copper sheet
End winding connections

## Slide 6
Implementation on AFPM
Air cored stator
  No attraction between rotor and stator
  Eliminated cogging torque
  Better demagnetization performance
  Low magnetic loading
Stackable in the axial direction
  Multi-staged designs
  Increased modularity
Eliminated AC losses on rotor
  Except ones due to armature reaction
Topology advantages
Single turn of flat winding with rotor
Induced voltage on the flat winding
The proposed topology
Notes: Topolojiyi anlat
AFPM, double rotor single stator, sandwiched
Diagonal placement
N42M grade magnets

## Slide 7
Flat winding and implementation on AFPM
Analytical modeling
Experimental verification
1 MW wind turbine generator
Conclusions
Outline

## Slide 8
Magnetic Field Modeling
[5,6]
Magnet approximation
Field modeling
Magnetization of the magnets
Notes: No-load magnetic field
Magnetic scalar potential with the help of Fourier series, Laplace eqns and boundary cd
2D representation of the model is needed, thus magnet approximation
Field derivation steps
Fourier representation of the permanent magnets
Laplacian of magnetic scalar potential = 1/mr * divergence of magnetization vector
At both regions, laplacian of magnetic scalar potential is zero
  In air region, there is no magnetization source
  In magnet region, there is only y-component, which depends on x-variable, thus, divergence of magnetization is zero
The solution is governed by laplace equation
H (magnetic field intensity) is minus gradient of magnetic scalar potential
B (flux density) is related to H via constitutive relation
Solve unknowns with boundary conditions
  No magnetic field beyond Neumann boundaries
  B normal and H tangential are continious at boundaries
Solve the equation in MATLAB with matrix inversion tool and obtain the field.

## Slide 9
Magnetic Field Modeling
Verification by FEA
Parameters | Value
Rated power | 1 MW
Rotational speed | 20 rpm
Diameter | 4.8 m
Number of poles | 46
Magnet grade | N42M
Remanence flux density | 1.29 T
Magnet thickness | 36.5 mm
Magnet to magnet distance | 47.3 mm
3%
Magnetic flux density distribution by FEA
Dummy machine for field verification

## Slide 10
Other Parameters
Induced voltage and torque
 | Conduction loss | Eddy current loss
Analytical model | 75.54 kW | 33.17 kW
FEA | 75.56 kW | 31.39 kW
Conduction and eddy current losses
5.7%
<0.1%
[7]
Notes: Peddy α t2, f2, B2, 1/res

## Slide 11
Deflection Analysis
Parameters | Value
Peak flux density | 0.87 T
Outer diameter | 300 mm
Air gap clearance | 2.3 mm
 | Deflection | Percentage of clearance
Analytical model | 40.4 µm | 1.76 %
FEA | 41.6 µm | 1.81 %
[8]
3%
[8] W. C. Young and R. G. Budynas, Roark’s formulas for stress and strain; 7th ed. McGraw Hill, 2002.
Deflection of rotor cores
Stress distribution approximation
Dummy machine for deflection verification
Deflection analysis comparison
Deflection analysis by FEA
Notes: The reason of deflection and deflection analysis onemi
Bending of the rotor cores
Mechanical problems - non-linearities in the magnetic model
Allowed deflection is 5-10% of the air gap clearance
Circular plate theory
Constant and uniform stress distribution
Mrb = unit radial bending moment
D = plate constant
Qb = shear force on the shaft
q= stress
FEA by SolidWorks on prototype machine
Resultant deflection = 2 %

## Slide 12
Flat winding and implementation on AFPM
Analytical modeling
Experimental verification
1 MW wind turbine generator
Conclusions
Outline

## Slide 13
Genetic Algorithm Optimization
Parameters | Value
Rated power | 1.4 kW
Line voltage | 48 V
Current | 20 A
Rotational speed | 525 rpm
Rated torque | 26 Nm
Pole number | 8
Frequency | 35 Hz
Outer diameter | 300 mm
Current density | 4 A/mm2
Magnetic loading | 0.6 T
Conduction loss | 110 W
Eddy current loss | 53 W
Efficiency | 89%
Active mass | 29 kg
Air gap clearance | 2.3 mm
Flat wire dimensions | 1 x 5 mm
Fully analytical optimization on MATLAB
Objective function of minimizing active mass
Optimization variables of
  Outer diameter
  Magnetic loading
Population and generation sizes of 50, both
[9] G. Cakal and O. Keysan, ‘‘A novel flat winding made of aluminum or copper sheet for axial flux machines,’’ IET Electric Power Applications, (Review), 2020.
[9]
Optimized prototype machine
Notes: IET Electric Power Applications
Table comments
1.4 kW, 48 V and 20 A
Relatively low voltage and high current
8 pole with 35 Hz frequency
4 A/mm2
Conduction > Eddy
  Due to thin conductor sheet
  Stacking through thickness
Optimization constraints (sorarlarsa)
Line voltage 48V
Current density 4A/mm2
Pole number 8
Remanence flux density 1.39 T
Air gap clearance 2.3 mm
Flat wire thickness 1 mm
Efficiency > 80%
Frequency <100 Hz

## Slide 14
Mechanical Design
Mechanical design
Assembling process
Mechanical design of the prototype
Assembly of the prototype
Notes: SolidWorks is used

## Slide 15
Manufacturing Stages
Laser cutting of copper sheet
Cut pieces
Bending of flat wires
Flat wire placement
Notes: Laser is used. Stamping press can be used also.
1 mm copper and aluminum thickness

## Slide 16
Manufacturing Stages
Copper flat wires
Isolation paper
Aluminum flat wires with isolation papers
Connectors at end winding
Notes: 240 flat wires are used
240 end winding soldering is done
For copper soldering is enough
For aluminum advanced solutions are needed

## Slide 17
Manufacturing Stages
Aluminum flat winding stator with terminals
Copper flat winding stator with terminals
Glass fiber in epoxy molding
Epoxy molding
Notes: Thermocouples for temperature measurement
Cam elyaf = glass fiber

## Slide 18
Manufacturing Stages
Epoxy molding
Stator inside the mold
Final form of the stator
Thermal testing
Notes: Epoxy molding
-high thermal conductivity
-low viscosity (akmaya karsi direnc)
-high mechanical strength

## Slide 19
Manufacturing Stages
ST52 rotor steel
Magnet guides on rotor disc
Assembling magnets with rotor core
Safe fingers after assembly
Notes: ST52 steel with Br 1.9 T
N42M NdFeB magnets

## Slide 20
Manufacturing Stages
Water jet cutting of mechanical structure
Assembling of two rotor discs
The prototype
Experimental setup
Notes: No forced cooling
Setup
Run as generator
Loaded by three phase resistor bank
Input power, torque and speed measured by torque transducer
Output power measured by wattmeter

## Slide 21
Experimental Results
Open circuit characteristics
Loading test
Eddy current and friction losses
Eliminated 3rd harmonics
2%
Full load, 26 Nm
Half load,13 Nm
Current harmonics due to unbalanced resistive load
At rated operation
  55 W of eddy current loss
  8 W of friction loss
Induced voltages
Voltage and current measurements
Eddy current and friction loss variation against speed
Harmonics of induced voltages
Notes: OC test
Rotated with prime mover
No-load 525 rpm
Loading test
4.6 % drop in voltage due to armature resistance
Eddy current and friction losses
Measured at rated speed
Friction loss measured without stator
No load losses=friction+eddy
Eddy exponential increase with square as expected

## Slide 22
Experimental Results
Losses and efficiency measurement
 | Analytical model | Experimental result
Eddy current loss | 53 W | 55 W
Conduction loss | 110 W | 117 W
Phase resistance | 93 mΩ | 100 mΩ
Efficiency | 89 % | 88 %
4%
6%
Thermal characteristics
7 A/mm2 for flat wire under natural cooling
63 W eddy and friction
117 W conduction (4 A/mm2)
ΔT = 32 °C
63 W eddy and friction
359 W conduction
ΔT = 75 °C
32 °C
17 °C
Temperature measurement over time
Notes: Losses and efficiency measurement
Under rated operation
Eddy current loss difference due to 2% field error
Conduction loss difference due to cable resistance of measurement devices (20A)
Thermal characteristics
Winding temperature only
Ambient temperature of 27 C

## Slide 23
Copper vs. Aluminum Flat Winding
Copper
Merits | 63% more conductive | 70% lighter 70% cheaper
Challenges | High eddy current losses | Welding/soldering
Aluminum
[7]
Eddy current losses
The variation of eddy current loss against speed
Notes: Feasibility of aluminum
Aluminum is not common in stranded round wires because conduction > eddy
For flat wire, cross sectional area ↑, AC losses ↑ so investigate the aluminum
Al is 70% cheaper per mass
Both are manufactured for the prototype machine
Copper → simple soldering
Aluminum → TIG welding, laser welding, ultrasonic welding, spot welding(punto), tin plating then soldering
Resistivity ↑, skin depth ↑, AC losses ↓

## Slide 24
Copper vs. Aluminum Flat Winding
Copper
Aluminum
Copper
Aluminum
Conduction
losses
110 W
31 W
185 W
49 W
Eddy current
loss
53 W
199 W
34 W
124
W
Total losses
171
W
246
W
227
W
189
W
Efficiency
89.3%
85.3%
86.3%
88.3%
Winding mass
3.56 kg
1.08
kg
Material cost
$ 170
$ 12
+33%
-70%
-93%
Rated speed
(525 rpm)
High
speed
(1000 rpm)
Rated speed
(525 rpm)
High
speed
(1000 rpm)
-23%
Loss variations on torque speed plane
Efficiency maps
Material selection
Higher efficiency
Higher efficiency
Notes: Total losses including conduction and eddy current losses
Material selection
Experimentally verified at crossed points
At rated operation, copper is favorable
Case study table
Rated power of 1.4 kW both

## Slide 25
Demagnetization Analysis
-d axis current
80 °C operating temperature
Observation points inside magnet
Finite element analysis
Analytical results
No risk of demagnetization for the prototype
Short circuit at the terminals
800 A
Demagnetization curve of a PM
Demagnetization curve of PM at different currents
Direct and quadrature axes
Notes: Purpose of demagnetization analysis
Safe and reliable operation especially in field weakening
Air cored → reluctance high → inductance low → large sc current
Demagnetization sources
Large reverse magnetic field
High temperature
Aging of the magnet itself
No demagnetization risk
- Expected since low voltage and high current

## Slide 26
Flat winding and implementation on AFPM
Analytical modeling
Experimental verification
1 MW wind turbine generator
Conclusions
Outline

## Slide 27
Mechanical Design and Optimization
Shortened lever arm
Less deflection
Decreased structural mass
Increased torque density
Increased modularity
Mechanical design
[10]
Genetic algorithm optimization
Parameters | Value
Rated power | 1 MW
Rated speed | 20 rpm
Efficiency | > 90%
Line voltage | < 690 V
Parameters | Value
Diameter | 2 m – 13 m
Flat wire width | 5 mm – 50 mm
Flat wire thickness | 1 mm – 10 mm
Number of poles | 10 – 160
Current density | 1 A/mm2 – 9 A/mm2
Number of stages | 1 – 14
Number of parallel turns | 1 – 8
Variables
Constraints
Objective function
min(total mass)
Preferred mechanical models
Notes: The aim of the study
Observe the flat winding in MW-class machines
By upscaling the proposed models
Selected application
- Direct-drive axial flux wind turbine generator
The importance of structural mass estimation
- Diameter ↑, active mass ↓, structural mass ↑

## Slide 28
Genetic Algorithm Optimization
Parameters | Value
Rated power | 1 MW
Torque | 480 kNm
Rotational speed | 20 rpm
Diameter | 4.8 m
Number of stages | 2
Voltage | 680 V
Current | 850 A
Active mass | 10.4 t
Structural mass | 5.6 t
Total mass | 16.0 t
Efficiency | 90 %
Number of poles | 46
Frequency | 7.7 Hz
Current density | 3.8 A/mm2
Flat wire dimensions | 3 x 18.6 mm
Total cost | € 203k
Conduction loss | 75 kW
Eddy current loss | 31 kW
x 63
[11] G. Cakal and O. Keysan, ‘‘Axial flux generator with novel flat wire for direct-drive wind turbines,’’ IET Renewable Power Generation, (Accepted), 2020.
[11]
Feasibility
Material cost | € 45k
Laser cutting | € 1.2k
Water jet | € 8.5k
Optimized 1 MW generator
Cost analysis
Copper sheet
Notes: Table comments
Double stage, 1 MW 480 kNm with 4.8 m diameter
Total mass of 16 tons
Efficiency and voltage converged close to their limits
Current density 3.8 A/mm2, proven to be safe.
Around € 200k (two hundred thousand)
More cost-effective solutions when the cost is added to objective fcn
Feasibility
92 flat wires per sheet
Stamping press can decrease the cost further
Faster

## Slide 29
Comparison
 | Li et al. [12] | This study | McDonald et al. [13] | Maples et al. [14] | Versteegh [15] | Bang [16]
Generator type | RFPM | AFPM | AFPM | RFPM | RFPM | RFPM
Power | 0.75 MW | 1 MW | 1 MW | 1 MW | 1.5 MW | 2 MW
Speed | 29 rpm | 20 rpm | 12 rpm | 26 rpm | 18 rpm | 20 rpm
Torque | 250 kNm | 477 kNm | 798 kNm | 367 kNm | 796 kNm | 979 kNm
Number of stages | 1 | 2 | 4 | 1 | 1 | 1
Active mass | 3.1 t | 10.4 t | 18.6 t | - | 16.7 t | 14.6 t
Structural mass | - | 5.6 t | 6.9 t | - | 20.8 t | 10.4 t
Total mass | - | 16.0 t | 25.5 t | 17.4 t | 37.5 t | 25.0 t
Torque density by active mass | 79.7 Nm/kg | 46.0 Nm/kg | 42.9 Nm/kg | - | 47.7 Nm/kg | 67.0 Nm/kg
Torque density by total mass | - | 29.8 Nm/kg | 31.3 Nm/kg | 21.0 Nm/kg | 21.2 Nm/kg | 39.2 Nm/kg
Notes: Comments
Generators with power range 0.75 MW – 2 MW
The performance is compared in terms of torque density in Nm/kg
Not all publications have mass data
Two definitions of torque density
˷30 Nm/kg is compatible with other generators
The main advantage
Ease of manufacturing
The advantages of air cored design

## Slide 30
Thermal Analysis
SolidWorks simulation
106 kW heat power
  75 kW conduction loss
  31 kW eddy current loss
50 W/(m2K) convection
  Air cooling
ΔT = 90 °C
ΔT = 40 °C
66% increase in electrical loading
Partially coated epoxy
Increased surface area
Decreased thermal resistance
Actual model
Improved model
Flat winding stator of the generator
Full coating of the windings
Partial coating of the windings
Notes: On SolidWorks
Actual model
28 C ambient
118 C max temperature
3.8 A/mm2 safe
Improved model
Thermal conductivity
Copper = epoxy x 40
Direct contact to air
Less than half of temperature rise of actual model
Thermal conductivity
Copper 400 W/(mK)
Epoxy 1-10 W/(mK)
Water 0.6 W/(mK)

## Slide 31
Flat winding and implementation on AFPM
Analytical modeling
Experimental verification
1 MW wind turbine generator
Conclusions
Outline

## Slide 32
Conclusions
 | Flat winding | Conventional round winding | Hairpin winding | PCB winding
Ease of manufacturing | ++ | + | + | ++
Current density | ++ | - | + | ++
Current rating | ++ | + | ++ | -
Manufacturing cost | + | + | - | --
End winding loss | ++ | + | - | +
Eddy current loss | + | ++ | - | +
Boosted machine performance
  Ease of manufacturing
  Current density up to 7 A/mm2
  Shortened end windings
  Lower end winding losses
Experimental verification on 1.4 kW prototype
  Good agreement with analytical and FEA results
Elimination of eddy current losses
  Thin flat wire
  Stacking through thickness
Aluminum alternative
  At high speed operation
  Cost and weight advantages
Performance on MW-class
  Comparable torque density
Notes: Conventional windings may lack at some points
Alternative winding is needed
Table + first bullet
Ease of manufacturing
Laser cutter / stamping press
Higher current density (7 A/mm2)
High current rating
Shortened end windings
Implementation on axial flux machine
High torque density
No cogging torque

## Slide 33
[1] Taizhou Chuangpu Machinery and Electricity, “Basic knowledge of stator winding.” www.ixymotor.com, Accessed: 2020-08-19.
[2] Special Machine Tool, “Hairpin winding technology.” www.specialmachinetool.it. Accessed: 2020-08-19.
[3] Fraunhofer-Institute for Manufacturing Technology and Advanced Materials, "Coils produced by casting.” www.generativ.fraunhofer.de. Accessed: 2020-08-19.
[4] G. Cakal and O. Keysan, (2019). Elektrik Makinaları İçin Bir Sargı Yöntemi (Patent Pending). Türk Patent.
[5] Z. Q. Zhu, D. Howe, E. Bolte, and B. Ackermann, “Instantaneous magnetic field distribution in brushless permanent magnet DC motors. I. open-circuit field,” IEEE Transactions on Magnetics, vol. 29, pp. 124–135, Jan 1993.
[6] E. P. Furlani, “Computing the field in permanent-magnet axial-field motors,” IEEE Transactions on Magnetics, vol. 30, pp. 3660–3663, Sep. 1994.
[7] G. Muller, K. Vogt, and B. Ponick, Wicklungen Rotierender Elektrischer Maschinen. John Wiley & Sons Ltd., 2009.
[8] W. C. Young and R. G. Budynas, Roark’s formulas for stress and strain; 7th ed. McGraw Hill, 2002.
[9] G. Cakal and O. Keysan, ‘‘A novel flat winding made of aluminum or copper sheet for axial flux machines,’’ IET Electric Power Applications, (Review), 2020.
[10] M. A. Mueller and A. S. McDonald, “A lightweight low-speed permanent magnet electrical generator for direct-drive wind turbines,” Wind Energy, vol. 12,no. 8, pp. 768–780, 2009.
[11] G. Cakal and O. Keysan, ‘‘Axial flux generator with novel flat wire for direct-drive wind turbines,’’ IET Renewable Power Generation, (Accepted), 2020.
[12] H. Li, Z. Chen, and H. Polinder, “Optimization of multibrid permanent-magnet wind generator systems,” IEEE Transactions on Energy Conversion, vol. 24, pp. 82–92, March 2009.
[13] A. S. McDonald, N. Al-Khayat, D. Belshaw, M. Ravilious, A. Kumaraperumal,A. M. Benatamane, M. Galbraith, D. Staton, K. Benoit, and M. Mueller, “1MW multi-stage air-cored permanent magnet generator for wind turbines,” 6th IET International Conference on Power Electronics, Machines and Drives (PEMD 2012), pp. 1–6, 2012.
[14] B. Maples, M. Hand, and W. Musial, “Comparative assessment of direct drive high temperature superconducting generators in multi-megawatt class wind turbines,” Technical Report,National Renewable Energy Laboratory, pp. 1–40, 10 2010.
[15] C.Versteegh, “Design of the zephyros Z72 wind turbine with emphasis on the direct drive PM generator,” Nordic Workshop on Power and Industrial Electronics, pp. 1–7, 2004.
[16] D. Bang, Design of Transverse Flux Permanent Magnet Machines for Large Direct-Drive Wind Turbines. Phd dissertation, Delft University of Technology, Delft, The Netherlands, October 2010.
References

## Slide 34
Thanks!

## Slide 35
Additional Slides
Hot spot due to weak soldering
Temperature rise at different operating conditions

## Slide 36
Current Density Calculation
55 W eddy
8 W friction
117 W conduction
180 W total
ΔT = 32 °C
55 W eddy
8 W friction
422 W total
ΔT = 75 °C
359 W conduction
J = 4 A/mm2
117 W conduction
J = 7 A/mm2
359 W conduction

## Slide 37
Demagnetization Analysis
-d axis current
80 °C operating temperature
Observation points inside magnet
Finite element analysis
Analytical results
Risk of demagnetization
Short circuit at the terminals
2.5 kA
Use H or UH grade magnets
80 °C approximation
Demagnetization curve
Notes: Risk of demagnetization
Unlike the prototype

## Slide 38
Cost Analysis
 | Prototype machine | MW-turbine
Permanent magnets | € 320 | € 135k
Winding material | € 170 | € 45k
Rotor iron | € 45 | € 11k
Structural material | € 5 | € 12k
Total | € 540 | € 203k
 | Specific cost
Magnet | 60 €/kg
Copper | 15 €/kg
Rotor iron | 2 €/kg
Structural steel | 2 €/kg
Notes: Risk of demagnetization
Unlike the prototype

## Slide 39
Diagonal Placement
Diagonal magnet placement

## Slide 40
Optimization
Diameter variation
Flat wire thickness variation
Notes: In order to understand the tradeoffs between machine parameters, the outer diameter of the generator is fixed and an optimization study is conducted to find the optimum design. This procedure is repeated for seven different outer diameters from 2m to 8m. The optimum designs are obtained for each diameter and following results are obtained.
Procedure
The outer diameter is fixed
Seven optimization problems are solved
Diameter variation
Diameter ↑, lever arm ↑, PM mass ↓
Active mass ↓, structural mass ↑
Minimum mass around 5m
Importance of adding structural mass
Cost α PM mass → diameter ↑, cost ↓
Diameter ↓, induced volt ↓ (due to reduced linear speed) → multistage designs, → axial length↑
Flat wire thickness variation
Efficiency constraint → constant total loss
Thickness ↑, eddy loss ↑, conduction ↓
To limit eddy loss, frequency and pole number ↓
Conduction α J2, then to limit conduction loss, J ↓
Losses plot
All parameters are fixed
Only thickness is changed
Same volume and J → conduction loss same
Thickness ↑, eddy loss ↑